Parameters such as video frame number per second, sensitivity, TV mode of this device can be adjusted according to the user’s need. The default values are what we get from experiences and acceptable to most users. Therefore we suggest the user not revise them unless necessary.

When revision is necessary, please follow these procedures:

- Copy file system.txt (see user CD) to root directory of TF card.

- Open the file from root directory of TF card on a computer, and revise according to user’s actual need, then save the file(see ‘revision notes’ below)

- Take out the TF card and insert into the device

- Power on. When the “Finish” message is displayed, take out the card.

- Delete system.txt file on TF card. (If not deleted, the update process will be initiated every time)

- Insert TF card again into the device

- If parameters such as time is altered, please reset.

Revision notes of file system.txt

A 7-digit letter and number combination is included in this file. Revising the number can satisfy customer need.

E.g. F15V0S9

- The second and the third digits means frame number ranging from 00-30.  If the number is 15, it means 15 frames; 30 means 30 frames, 09 means 9 frames. (9 should be written as 09, otherwise there will be error). (default value is 15)

- The fifth digit means TV mode. 0=PAL，1=NTSC  (default value is 0)

- The seventh digit is video sensitivity ranging from 0-9, bigger number signifies higher sensitivity. (default value is 9)